## Slide 1: EPSCoR Greenhouse 9C
Summary:
  180 Raspberry Pi bramble above GH9C on a gantry in a grid formation.
  Goal: Capture and pull images autonomously then analyze pictures for phenotypic traits of plants in the greenhouse.

## Slide 2: Previous Efforts
Physical & Hardware:
  All Raspberry Pis placed on overhead gantry in a grid formation
  Power strips with adapters and USB cables connected to Raspberry Pis
    USB cable is Micro to Type A
    Very similar (almost identical) to most Android smartphone chargers
      Power adapter for Raspberry Pi provides exactly 5V, 1A
  WiFi Dongles attached for internet access
    Initially, Adafruit dongles used for the Raspberry Pi
    Changed to Element14 WiPi dongles because of WiFi issues
      More powerful signal and ability to hold a signal connected longer

## Slide 3: Current Efforts
  Physical & Hardware:
    The power strips and cables have remained the same, however, Stuart has made sure the power cables don’t have any loops to reduce electromagnetic interference
    WiFi dongles remain the same as the Element14 WiPi
    Stuart is changing the angle of the cameras in order to increase the resolution of the 3D reconstruction

## Slide 4: Previous Efforts cont.
Software & Management:
  Raspberry Pi used Debian Wheezy (Raspbian version)
  Quadrants of Raspberry Pis would reboot at scheduled times
  Ganglia installed on all the Raspberry Pis to have an overview of the bramble with a 5-second delay
  Any change to the bramble required changing each and every Raspberry Pi manually
    The scheduled reboots would cause management to be unduly difficult
  Pictures taken using cronjob on each Raspberry Pi independent of internet access
  Pictures pushed to the infrastructure by each Raspberry Pi also using cronjobs.
    Aside from files appearing on the infrastructure, no way to know how a file failed or if it failed to transfer

## Slide 5: Current Efforts cont.
  Software & Management
    Raspberry Pi now have Debian Jessie (Raspbian version)
      Raspbian has been integrated into the proper Linux branch making it a less experimental and more stable Linux OS with access to all the proper drivers
    All Raspberry Pis remain on at all times.
    Ganglia reinstalled on Raspberry Pis. All rPIs report to serverpi
    Pictures taken with cronjob on each of the Raspberry Pi independent of internet access
    Pictures pulled onto the infrastructure from each Raspberry Pi using a cronjob on chronos (DDPSC rsync server)
      Logs kept from each job when pulled from the bramble
    Using a deployment configuration engine called Ansible to manage the Raspberry Pi bramble from chronos
      Doesn’t require specialized setup on the Raspberry Pis aside from Python 2.7+ and ssh
      Can be installed via package manager or GitHub on the centralized server allowing for installation without administrator privileges

## Slide 6: WiFi Issues
  The majority of the problems with the system stem from connection to each Raspberry Pi for either short time spans or the amount of time it takes to transfer a file
  WiFi interference is the main cause of these issues
    There are numerous wireless access points (WAPs) stationed in and around the greenhouse that cause interference as well as the 180 rPIs themselves causing interference issues
  Current solutions to WiFi interference:
    We have two extra WAPs and four SSIDs being used exclusively for the bramble that stop the Raspberry Pis being dropped from the network
    The new WiFi dongles also help with stability of connection and ability to establish a connection
    Decrease transmit power from each Raspberry Pi until it’s time to transfer files then up the transmit power for the duration of transfer time
  Possible solutions to WiFi interference:
    As recommended by IT, wire every Raspberry Pi to a switch that is directly connected to the internet
      No WiFi, no interference
    Halfway wire the Raspberry Pis, six at a time to a wireless bridge bringing the number of devices connected to each SSID/WAP to around 8 per SSID instead of 45 per SSID
    If each Raspberry Pi has to be wireless and not just the entire system, then we can get WiFi dongles with directional antennas

## Slide 7: WiFi Issues cont.
  In order to reduce the amount of data transferred between the Raspberry Pis and the centralized server:
    Removed reverse DNS lookup in SSH
    SSH authorization is assumed to be correct instead of verified
    All the Raspberry Pi IP addresses are assumed to be the correct ones and given to the correct machines
    UTMP is disabled on the Raspberry Pis
    Enabled ControlMaster for SSH which keeps an established connection open so multiple commands can use the same connection
  RSH can be used, but is more insecure than SSH even with all the previous changes

## Slide 8: SD Cards: Labeled!

## Slide 9: Management of Raspberry Pi bramble
  To manage the bramble, Ansible needs a list of host names or IP addresses
    All of the rPIs have been given static IP addresses ranging from 10.9.0.11 to 10.9.0.190
    They are spaced out in a grid pattern and given their IP addresses in that order.
    The IP addresses are also translated into grid matrix coordinates (2D array instead of 1D array coordinates)

## Slide 10: Raspberry Pi Bramble: Octet and Grid Forms

## Slide 11: Management of Raspberry Pi bramble
  Ansible uses playbooks to execute plays that are then executed on all or a limited number of hosts
  I made several playbooks to handle:
    Taking test pictures
    Copying pictures from the bramble
    Transferring the picture taking python script
    Changing all of the SSH options (and reverting changes)
  A full documentation of the process from initial SD cards to fully setup Ansible management can be found at my github:
    https://github.com/calizarr/EPSCoR_Bramble_GH9C/

## Slide 12: Adding GPS units to images
  During the 3D reconstruction process, we found out that VisualSFM can use GPS data.
  I chose a spot in Greenhouse 9C found its GPS coordinates, measured the distance from the spot to ShakoorCamera145.
    Using ShakoorCamera145 as an origin, I used QGIS and PyQGIS to reconstruct the positioning of the bramble as a matrix
  Stuart measured the corners of the greenhouse and found their coordinates as well as the distance from the northeast corner to ShakoorCamera21
    Reconstructed bramble as matrix using ShakoorCamera21 as the origin.
  Still a work in progress, but it should allow the 3D reconstruction to use real units when scaling and therefore allow us to measure items in the reconstruction

## Slide 13: QGIS Overlay (Google Maps Hybrid)

## Slide 14: Raspberry Pi Cluster On QGIS
Stuart’s Coordinates
César’s Coordinates

## Slide 15: Results
  165 Raspberry Pis are consistently reporting and establishing connections. Between 170-172 occasionally establish connection
  Initial 3D reconstructions exist and as camera positions and angles are finalized, we keep improving them
  Fully documented process

## Slide 16: 3D Reconstruction

## Slide 17: 3D Reconstructions: Connected Components

## Slide 18: Next Steps
  Adding GPS units to image files to aid in 3D reconstruction
    Also have proper units and scale for the 3D reconstruction
  Finalize camera angles and positions to improve 3D reconstruction
  Set the bramble to run autonomously
  Take 3D reconstruction point cloud and analyze subsections (plants) to extract phenotypes